a.)

b.)
Switch Position	Switch	Voltage	Current
1	1	V_{S1} = 0	I_{S1} = i_L
1	2	V_{S2} = 0	I_{S2} = i_L
1	3	V_{S3} = V_g - v	I_{S3} = 0
1	4	V_{S4} = V_g	I_{S4} = 0
2	1	V_{S1} = V_g	I_{S1} = 0
2	2	V_{S2} = V_g - v	I_{S2} = 0
2	3	V_{S3} = 0	I_{S3} = -i_L
2	4	V_{S4} = 0	I_{S4} = -i_L

c.)

d.)
Switch Position	Switch	Voltage	Current
1	1	0	+/-
1	2	0	+/-
1	3	+	0
1	4	+	0
2	1	+	0
2	2	+	0
2	3	0	+/-
2	4	0	+/-

Output voltage ratio ranges from (-\infty, 1] , thus V can only be as large as V_g .

Switch voltage equals V_g - V so it is always greater than or equal to 0.

Polarity doesn’t vary with duty cycle.

Inductor current ratio ranges from (-\infty, 1] .

Switch current is a function of inductor current only so polarity varies with the duty cycle.

e.)

All switches are current-bidirectional two-quadrant. They can be realized with a power MOSFET.
a.)

b.)
Switch Position	Switch	Voltage	Current
1	1	V_{S1} = 0	I_{S1} = i_L
1	2	V_{S2} = 0	I_{S2} = i_L
1	3	V_{S3} = v	I_{S3} = 0
1	4	V_{S4} = v	I_{S4} = 0
2	1	V_{S1} = -v	I_{S1} = 0
2	2	V_{S2} = -v	I_{S2} = 0
2	3	V_{S3} = 0	I_{S3} = i_L
2	4	V_{S4} = 0	I_{S4} = i_L

c.)

d.)
Switch Position	Switch	Voltage	Current
1	1	0	+
1	2	0	+
1	3	+/-	0
1	4	+/-	0
2	1	+/-	0
2	2	+/-	0
2	3	0	+
2	4	0	+

Output voltage ratio ranges from (-\infty, -1) and (1, \infty) .

Switch voltage is a function of output voltage only so polarity varies with the duty cycle.

Inductor current ratio ranges from (1, \infty) .

Switch current is a function of inductor current so polarity doesn’t vary with the duty cycle.

e.)

All switches are voltage-bidirectional two-quadrant. They can be realized with a series BJT transistor and diode.

a.)

b.)
Switch Position	Switch	Voltage	Current
1	1	V_{S1} = 0	I_{S1} = i_{L1} + i_{L2}
1	2	V_{S2} = V_g - v_{C1}	I_{S2} = 0
2	1	V_{S1} = V_g - v_{C1}	I_{S1} = 0
2	2	V_{S2} = 0	I_{S2} = -(i_{L1}+i_{L2})

c.)

d.)

Switch Position	Switch	Voltage	Current
1	1	0	+
1	2	+	0
2	1	+	0
2	2	0	-

Output voltage ratio ranges from (0, -\infty) .

Switch voltage is a function of V_g - V so polarity doesn’t vary with the duty cycle.

Inductor current ratio ranges from (0, \infty) .

Switch current is sum of inductor currents so polarity doesn’t vary with the duty cycle.

e.)

All switches are single quadrant. They can be realized by a BJT transistor.