Constants	Value
\mu_0	4\pi \cdot 10^{-7} H/m
\rho \ [23C]	1.724 \cdot 10^{-6} \Omega
\rho \ [100C]	2.3 \cdot 10^{-6} \Omega

Buck Converter	Requirement
f_s	50 kHz
V_g	40 V
V	20 V
R	\geq 4 \Omega
\Delta i_L	10% I_{DC}

a.)

b.) I_{max} is the sum of the inductor current I, the ripple current (10%), and a safety factor (15%).

c.)

Inductor	Requirement
B_{max}	0.25 T
K_u	0.5
P_{cu}	1W

1.

Core size must be greater than 0.29 (cm5).

2. Air gap is dependent upon the core cross-sectional area A_c . Due to the core size constraint, the possible cores are EE30, EE50, EE60, and EE70/68/19.

For this design, core EE30 is chosen with cross section area 1.09 cm2.

	Geometric Constant (Kg)	Cross-sectional Area (Ac)	Core Window Area W_A	MLT
EE30	0.857 cm5	1.09 cm2	0.476 cm2	6.6 cm

3. Plug in values from previous steps.

4. Design uses the largest wire size given constraints. The wire size is calculated to be less than or equal to 0.005 cm2, so a 21 AWG wire is chosen.