EE 452 – Power Electronics Design
Experiment 1 Pre-lab Assignment: Part C
Department of Electrical & Computer Engineering
University of Washington
# Introduction
The purpose of this assignment is to prepare you to conduct Experiment 1C. Please make sure you have read and understand the experimental procedure before attending your designated lab section.
This assignment will be due at the beginning of your lab section. Like your homework, you will submit the prelab assignments through Canvas. For each problem, please provide written analysis where appropriate, show your work, and clearly label all plots, if any.
# Parts
Experiment 1 will be done on the PCB using the following parts. In the electronic version of this document, you may click on the hyperlink embedded in the “Part number” column to bring up the data sheet for a given part. In addition to the components below, this experiment will also require resistors and capacitors of your choosing.
Description	Manufacturer	Part number
Power MOSFET	Infineon Technologies	IRFB4615PbF
Power MOSFET	Texas Instruments	CSD19535KCS
Half-bridge Gate driver	Infineon Technologies	IRS2184PBF
PWM Controller	Texas Instruments	UC3525AN

# Prelab tasks
Component familiarization. Using the applicable data sheets, determine the following (10 pts):
    - The drain-to-source resistance of both power MOSFETs in the on state.
Power MOSFET	Drain-to-Source Resistance
IRFB4615PbF	32 m \Omega
CSD19535KCS	3.4 m \Omega

    - The threshold gate-to-source voltage of the power MOSFETs.
Power MOSFET	Gate-to-Source Voltage
IRFB4615PbF	3 V
CSD19535KCS	2.7 V

    - The rated drain current of the MOSFETs.
Power MOSFET	Drain Current (@25C)
IRFB4615PbF	35 A
CSD19535KCS	150 A

    - The gate charge of both power MOSFETs
Power MOSFET	Total Gate Charge (@ VGS = 10V)
IRFB4615PbF	26 nC
CSD19535KCS	78 nC

- The rise and fall times of both power MOSFETS
Power MOSFET	Rise Time	Fall Time
IRFB4615PbF	35 ns	20 ns
CSD19535KCS	15 ns	5 ns

- The minimum logic high input voltage of the gate driver.
  VIH = 2.5V
Possible PWM frequency (5 pts) Using data from q1, compute the maximum possible switching frequency for both MOSFETS.
[skip]

GRAD STUDENTS REQUIRED: Bootstrap circuit design. (10pts) Study the UCC27712 gate driver datasheet. This datasheet has better guidance than the IRS 2184.
Compute the following for each MOSFET with a 5% boot capacitor ripple voltage.
  1. Bootstrap capacitance
  1. Bootstrap resistance (assuming a boostrap diode peak current of 3A)
  2. Consider: why do we need a bootstrap capacitance? (just for learning)
5% ripple voltage of 12V = 0.6V
IRS2184PBF Half-Bridge Gate Driver: I_{QBS} = 60uA

SB3H100 Diode: V_{DBOOT} = 0.8

Q_{TOTAL} = Q_C + \frac{I_{QBS}}{f_{SW}}

C_{BOOT} = \frac{Q_{TOTAL}}{\Delta V_{BOOT}}

R_{BOOT} = \frac{V_{DD}-V_{DBOOT}}{I_{DBOOT}}

Power MOSFET	Q_{TOTAL}	Boot Capacitance	Boot Resistance
IRFB4615PbF	26 nC + \frac{60uA}{50kHz} = 27.2 nC	27.2 nC / 0.6 = 45.3 nC	(12-0.8)/3 = 3.73\Omega
CSD19535KCS	78 nC + \frac{60uA}{50kHz} = 79.2 nC	79.2 nC / 0.6 = 132 nC	(12-0.8)/3 = 3.73\Omega

Bootstrap capacitance used in circuit will be at least twice as large as calculated
values as mentioned in datasheet.

CSD19535KCS
IRS2184PBF

UCC27712
TI Bootstrap Circuitry